## Slide 1
Note: Using this slide as a tool for making crossing gates requires some working knowledge of PowerPoint or another compatible presentation graphics tool.
The following slide contains images of crossing gate arms, counterweights, and base units. It is roughly HO scale but measurements are provided that were taken from a magazine article in Railroad Model Craftsman.
The image of the gate arm can be lengthened or shortened as needed for different length gates. Select the gate arm and use the size function to adjust object size to increase the length – just length, not height. Note that total length of the object, because it is made up of various polygons stitched together, is longer than the arm. Most presentation tools have a scale at the top and side of the work area that can be used to set the proper length in inches.
All the images may also be resized to other scales by using the size adjustment function for both length and height by a percentage:
Scale Adjustment
O 1/48 181.5%
S 1/64 136%
N 1/160 54%
Z 1/220 39.5%

## Slide 2: A scalable image
This image is very close to HO scale and not copyrighted.
It is available as a Powerpoint slide on the NCR Clinton River Division (Division 8) website http://div8.ncrnmra.org. Scroll down to and select the “Presentations” tab. Then select “A Scaleable Crossing Gate Image in Powerpoint format”.
By selecting the gate arm, it can be adjusted in length in Powerpoint
Drawing objects can be enlarged or reduced as needed for other scales
The gate arms and bases should be copied to a blank Powerpoint slide to adjust the length. The images may then be duplicated to have multiple images on one sheet of paper or slide material.
Dimensions as measured on original RMC drawing:
Base of arm: 12”
Tip of arm: 4”
Length of arm: 26’
Width of counterwgt 32”
Diameter counterwgt 12”
Height of cabinet 4’9”
Width of cabinet 27”
Thickness of cabinet 10”
In assembly, the crosshatch on the counterweight arm overlaps behind gate arm